## Slide 1: MVT 2023 Energy Management Algorithm
National Taipei University of Technology
Vehicle Engineering
Advanced Vehicle Control Lab Advisor：Professor Bo-Chiuan Chen
Student：林暐鈞, 吳祈陞, 陳乃維
2/2/2023

## Slide 2: Outline
Introduction
Recent Literature
Integrated Control Strategy
Torque Allocation
Energy Storage System Power Control
Conclusion

## Slide 3: Introduction
Hybrid energy storage system: Fuel cell/ Li-ion battery
Multi-actuators: Three motors
Goal: design EMA that controls motor torques, fuel cell current to minimize energy consumption, battery degradation while not violating some constraints

## Slide 4: Motor Torque Control Purpose
Axle distribution/Torque vectoring
  Trade-off between tire loss and motor loss
The battery temperature and degradation should also be taken into consideration

## Slide 5: Motor Power Loss
Four types of motor power loss
  Inverter and copper loss depend on q axis current
  Iron and friction loss depend on motor speed
Overall power loss

## Slide 6: Tire Power Loss
Tire energy dissipation
  Up to 7% of total energy
Tire power loss model
  Load transfer is neglected

## Slide 7: Outline
Introduction
Recent Literature
Integrated Control Strategy
Torque Allocation
Energy Storage System Power Control
Conclusion

## Slide 8: Recent literature - 1
MPC allocation is a popular method in recent literatures
Two step optimization method
H. Jing, F. Jia and Z. Liu, "Multi-Objective Optimal Control Allocation for an Over-Actuated Electric Vehicle," in IEEE Access, vol. 6, pp. 4824-4833, 2018, doi: 10.1109/ACCESS.2017.2788941.

## Slide 9: Recent literature - 2
Power optimization/ Tire power loss…are considered
Multi-purpose integrated control strategy are main focus

## Slide 10: Outline
Introduction
Recent Literature
Integrated Control Strategy
Torque Allocation
Energy Storage System Power Control
Conclusion

## Slide 11: AVCL Integrated Control Strategy
Control input
Axle Distribution
Motor Power loss Minimization
Model Predictive Control
Allocation
Speed controller
Tire Energy Dissipation
Minimization
Estimators
Road information
Model Predictive Power Management
Energy storage
Actuators
Motor F
Motor RL
Motor RR
Fuel Cell&H2 Tank
Battery
DC BUS

## Slide 12: Outline
Introduction
Recent Literature
Integrated Control Strategy
Torque Allocation
Energy Storage System Power Control
Conclusion

## Slide 13: Model Predictive Control Allocation
Cost function
Multi-purpose optimization
  Handling / lateral stability
  Tire energy dissipation
  Torque command change rate penalty
  Motor power loss (axle distribution torque command)
  Track the demand torque from speed controller
  Actuator physical limits

## Slide 14: Prediction Model - 1
State space model
x
u
w
y

## Slide 15: Prediction model - 2
Discretization
Online optimization using quadratic programming
  This model are also tested in 4WID control
  For certain parameter pair, it is better than hierarchy control strategy

## Slide 16: Motor Power Loss Minimization
Cost function
  Formulated based on the model of their power loss model
Off-line nonlinear optimization
  3D look-up table
Axle Distribution
Motor Power loss Minimization

## Slide 17: Tire Energy Dissipation Minimization
Tire model by their paper
Weighting design: use the estimated tire power loss at k-1 to adjust dynamically

## Slide 18: Outline
Introduction
Recent Literature
Integrated Control Strategy
Torque Allocation
Energy Storage System Power Control
Conclusion

## Slide 19: Battery EMA Version log
Version | Description
V0 | Initialization MPC model
V0.1 | Changed the R_delta weighting
V0.2 | Pmax is modified to be based on the product of Ifc_max and true voltage
V0.3 | Added the low-efficiency zone strategy
V0.4 | Changed Yref to gap tracking between SoCfc and SoCbat
V1.0 | Added variable weight strategy

## Slide 20: Energy Storage System Power Control
Problem formulation – minimize the cost function
Battery SoC tracking when FC SoC is enough
FC power penalty/ power change rate penalty
Track the demand load power

## Slide 21: Energy Storage System Power Control
= 7, = 3, ,
: Load power
: SOC difference ref.
Weighting
  SoC tracking
    When SoCbat < SoCbat low limit:1 (Load power tracking)
    When SoCbat > SoCbat low limit:500k(SoC tracking)
  Fuel cell power tracking: 0.1
  Fuel cell power change rate: 0
  Demand load power tracking: 1

## Slide 22: Power control-oriented model
Discrete model
Parameters
x

## Slide 23: Battery EMA
Model Predictive Power Management
  Predictive model
  QP solver
Weighting Control Strategy
  Weighting change strategy
  Hysteresis window
Eff. Power Control Strategy
  Low eff. limit
  AlphaFC convert

## Slide 24: Only Battery EMA test results
J average below the baseline 23%
  J_energy average below the baseline 0.32 kWh
  J_SoC average below the baseline 5298.7 sec
  J_Temp average below the baseline 3.98 deg
  J_deg average below the baseline 0.005 mAh/cycle
  J_v average above the baseline 57 s
  J_tire average below the baseline 2.56 Wh
Track | JE | JS | JT | JD | JV | JT | J
1 | 9.9213 | 10208.26 | 0 | 0.0004 | 6762.7668 | 76.822 | 0.7693
2 | 9.6703 | 0 | 0 | 0.0004 | 0 | 94.169 | 0.9329
3 | 11.0545 | 7985.49 | 0.8013 | 0.0005 | 809.8524 | 223.4199 | 0.8095
4 | 2.3406 | 0 | 0 | 0.0009 | 0 | 12.4427 | 0.6687
5 | 8.9133 | 632.25 | 19.3363 | 0.0506 | 109.2686 | 161.1183 | 0.9111
6 | 6.881 | 292.49 | 0 | 0.0009 | 0 | 233.8156 | 0.7377
7 | 3.5689 | 0 | 0 | 0.0011 | 0 | 186.823 | 0.7167
8 | 10.1949 | 1676.76 | 0 | 0.0006 | 967.8447 | 447.165 | 0.671
9 | 1.4706 | 0 | 0 | 0.0007 | 0 | 66.1595 | 0.6815
10 | 10.7609 | 1190.94 | 3.3007 | 0.0009 | 567.0538 | 573.3547 | 0.7592
Better
Worse

## Slide 25: Outline
Introduction
Recent Literature
Integrated Control Strategy
Torque Allocation
Energy Storage System Power Control
Conclusion

## Slide 26: Conclusion
The first version of torque allocation is done.
The first version of power distribution for hybrid energy storage is done, and the results are better than the baseline.